## Slide 1
State-of-the-Art Methods for Heart Rate and Blood
Pressure Estimation from PPG Signals
A Strictly Verified Literature Review | PPG-DaLiA & PulseDB Benchmarks | Deep Learning & Signal Processing
Biomedical AI Research Report | March 2026 | Verified Citations Only

## Slide 2
Presentation Overview
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
01
Why PPG-Based Cardiovascular Monitoring Matters
02
PPG Signal Fundamentals — Physics, Waveform & Artifacts
03
PPG-DaLiA Dataset — Structure, Protocol & Activities
04
HR Estimation: PPG-Only Methods & Benchmarks
05
HR Estimation: PPG + Accelerometer Methods
06
PulseDB Dataset — Scale, Signals & Evaluation Protocols
07
Blood Pressure Estimation on PulseDB
08
Comparative Analysis & Performance Trends
09
Research Challenges & Open Problems
10
Future Research Directions

## Slide 3
Why PPG-Based Cardiovascular Monitoring?
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
17.9M
CVD Deaths / Year (WHO)
>1B
Hypertension Sufferers Globally
~$500B
Annual CVD Economic Burden (US)
Green LED
PPG Technology in Smartwatches
No Cuff
Non-Invasive, Continuous BP Goal
Key Advantages of PPG Wearables
Miniaturized optical sensors already integrated into commercial wearables
Continuous, unobtrusive monitoring without clinical intervention
Rich physiological information: HR, SpO2, respiratory rate, vascular stiffness
Lower cost and complexity vs. ECG holter monitors
Clinical Need — Unmet Goals
Ambulatory HR estimation degraded by motion artifacts (wrist movements)
Cuffless BP estimation: <5 mmHg accuracy required — not yet achieved reliably
Generalization across diverse populations remains an open problem
Subject-to-subject variability in skin tone, vessel geometry limits models

## Slide 4
PPG Signal: Physics & Waveform Components
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
Measurement Physics
LED (green 520 nm) emits light through wrist tissue
Photodetector measures reflected or transmitted light intensity
AC component (~1-4%) reflects pulsatile blood volume changes per heartbeat
DC component (~99%) reflects static tissue absorption
Beer-Lambert law governs light attenuation by hemoglobin concentration
Empatica E4: green LED PPG, 64 Hz, single channel
Clinical pulse oximeters: red + infrared LEDs for SpO2
Waveform Components & Motion Artifacts
Systolic Peak
Max amplitude — rapid ventricular ejection into aorta
Dicrotic Notch
Brief dip — aortic valve closure at end-systole
Diastolic Wave
Secondary rise — reflected arterial pressure wave
APG Waves (a-e)
Second derivative features encoding arterial stiffness
Motion Artifacts
Wrist/arm movements introduce noise 10x cardiac amplitude
MA Mechanism 1
Mechanical displacement of sensor-skin interface
MA Mechanism 2
Arm venous pooling changes DC baseline

## Slide 5
PPG-DaLiA Dataset — The Standard HR Benchmark
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
15
Subjects (8F / 7M)
8
Daily Activities
64 Hz
PPG Sampling Rate
36h+
Total Recording Time
700 Hz
ECG Ground Truth
LOSO
Evaluation Protocol
Wrist Device: Empatica E4
• PPG: 64 Hz, green LED, single channel
• 3-axis Accelerometer: 32 Hz
• Commercial wristband, popular in research
Chest Device: RespiBAN Pro
• ECG: 700 Hz (gold standard HR reference)
• Used only for ground truth extraction
• NOT available during inference
Subjects: Demographics
• Age range: 21–55 years
• Varied fitness levels, body types
• Mix of indoor and outdoor activities
8 Activity Protocol:
1. Sitting (resting)
2. Ascending/Descending Stairs
3. Table Football (moderate motion)
4. Cycling
5. Driving a Car
6. Lunch Break / Eating
7. Walking
8. Working at Desk
Why LOSO Matters: Session-optimized MAE can reach 1-2 bpm, creating false sense of solved performance. LOSO (leave-one-subject-out) gives true generalization estimate.

## Slide 6
HR Estimation: PPG-Only Methods on PPG-DaLiA
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
TABLE 1 — PPG-Only Models (no accelerometer input)
Model
Authors
Year
Architecture
Protocol
MAE (bpm)
RMSE
Venue
CorNET
Biswas et al.
2019
2×CNN + 2×LSTM (PPG only, personalized)
Subject-dependent
N/R for DaLiA
N/R
IEEE TBCAS
BeliefPPG
Bieri et al.
2023
CNN encoder + Probabilistic Graphical Model (belief propagation)
LOSO
3.57 ± low SD
N/R
UAI 2023 (PMLR)
ResNet50-TL
Dark et al.
2022
ResNet50 + ImageNet transfer learning + STFT 2D input
LOSO
N/R explicitly
N/R
UbiComp 2022 (ACM)
SPEAR (self-supervised)
Ghorbani et al.
2024
Self-supervised denoising autoencoder + CNN HR
Out-of-dist. test
5.36 (OOD)
N/R
HDSR (Harvard)
Key Insight: BeliefPPG
BeliefPPG (2023) achieves 3.57 bpm LOSO MAE on PPG-DaLiA — competitive with PPG+ACC methods — by modeling heart rate as a hidden Markov process with temporal transition priors. It adds uncertainty quantification: removing top 1% uncertain predictions reduces MAE by a further 15%. Architecture: CorNET backbone + frequency-domain U-Net + belief propagation temporal smoothing. Citation: arXiv:2306.07730, UAI 2023, PMLR 216:173–183.
N/R = Not Reported | LOSO = Leave-One-Subject-Out | All citations verified: IEEE Xplore, arXiv, ACM DL, PMLR

## Slide 7
HR Estimation: PPG + Accelerometer Methods on PPG-DaLiA
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
TABLE 2 — PPG + Accelerometer Models
Model
Authors
Year
Architecture
Protocol
MAE (bpm)
Venue
CNN Ensemble (DeepPPG)
Reiss et al.
2019
CNN ensemble on STFT spectrograms of PPG+ACC
LOSO
~7.0 (31% vs SpaMaPlus)
Sensors MDPI
SpaMaPlus (classical)
Reiss et al.
2019
Sparse spectral decomposition + peak tracking (no DL)
LOSO
~9.0
Sensors MDPI
Q-PPG (NAS-TCN)
Burrello et al.
2021
Temporal Conv. Network (Neural Architecture Search, quantized)
LOSO
4.41
IEEE TBCAS
Embedding TCN (ActPPG)
Burrello et al.
2022
NAS TCN family + adaptive multi-model selection
LOSO
3.84
ACM HEALTH
PULSE
Kasnesis et al.
2025
Lightweight TCN + multi-head cross-attention (sensor fusion)
LOSO
4.03
IEEE JBHI
EnhancePPG
Benfenati et al.
2025
Modified PULSE + self-supervised pre-training + augmentation
LOSO
3.54 ★ BEST
AICAS 2025
Performance Evolution 2019→2025 (LOSO MAE on PPG-DaLiA):
SpaMaPlus ~9.0 → CNN Ensemble ~7.0 → Q-PPG 4.41 → Embedding TCN 3.84 → PULSE 4.03 → EnhancePPG 3.54 bpm [60% improvement over 6 years]

## Slide 8
PulseDB Dataset — Large-Scale BP Benchmarking
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
5,361
Total Subjects
5.2M+
10-sec Segments
125 Hz
Sampling Rate
2 Sources
MIMIC-III + VitalDB
10 sec
Segment Duration
Source 1: MIMIC-III (ICU)
• PhysioNet ICU database (USA)
• Invasive ABP, ECG, PPG waveforms
• Diverse pathological hemodynamics
• Citation: Johnson et al., Sci. Data 2016
Source 2: VitalDB (OR/ICU)
• Korean ICU/OR database
• Continuous physiological monitoring
• Demographic info available (age, sex)
• Citation: Lee et al., Sci. Data 2022
Signals Available
• ECG (electrocardiogram)
• PPG (photoplethysmography)
• ABP (invasive arterial BP waveform)
• 1st (VPPG) & 2nd (APPG) PPG derivatives
• Characteristic points pre-annotated
Three Testing Protocols (Critical for Fair Comparison):
Calibration-Based
Training & test subjects overlap.
Model sees per-subject reference data.
MAE ~9–10 mmHg (SBP) achievable.
Calibration-Free
Completely unseen test subjects.
True population generalization.
MAE rises to ~14 mmHg (SBP).
AAMI Protocol
Standardized clinical validation.
Requires specific BP distribution.
Target: <5 mmHg MAE, <8 mmHg SD.
Citation: W. Wang et al., 'PulseDB,' Front. Digital Health, 4:1090854, 2023. DOI: 10.3389/fdgth.2022.1090854

## Slide 9
HR Estimation on PulseDB — Why No Table?
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
Table 3 Status: No Published HR Benchmarks on PulseDB as Primary Dataset
PulseDB was explicitly designed and released as a blood pressure estimation benchmarking dataset — not for heart rate.
The dataset provides ABP waveforms for beat-to-beat SBP/DBP ground truth extraction. ECG is included as a secondary reference signal for BP model performance.
HR can be derived from ECG (standard peak detection), but this is used internally for data quality validation — not as a published benchmark target.
No peer-reviewed publications were found that use PulseDB as the primary evaluation dataset for PPG-based HR estimation.
The ICU-based population (MIMIC-III, VitalDB) and highly dynamic BP hemodynamics make PulseDB less suitable for ambulatory HR studies typically evaluated on consumer wearable datasets like PPG-DaLiA.
Researchers interested in PPG-based HR estimation should use PPG-DaLiA (ambulatory), WESAD (stress/affect), or the IEEE Signal Processing Cup datasets as established benchmarks.
Future work: PulseDB's ECG annotations could support a clinical HR estimation benchmark in ICU settings — an unexplored direction.

## Slide 10
BP Estimation on PulseDB — Deep Learning Results
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
TABLE 4 — Blood Pressure Estimation on PulseDB (Verified Results Only)
Model
Authors
Year
Input
Architecture
Protocol
SBP MAE (mmHg)
DBP MAE (mmHg)
1D ResNet-18 (demo)
Wang et al.
2023
PPG+ECG
1D ResNet-18 (modified)
Calibration-based illustration
Not Reported
Not Reported
XResNet1d101 (Calib)
Moulaeifard et al.
2025
PPG only
XResNet1d101 (1D, 101 layers)
Subject-specific calib.
9.4 ★
6.0 ★
XResNet1d101 (Free)
Moulaeifard et al.
2025
PPG only
XResNet1d101 (1D, 101 layers)
Calibration-free
14.0
8.5
XResNet1d101 (OOD)
Moulaeifard et al.
2025
PPG only
XResNet1d101 (external test)
Out-of-distribution
15.0–25.1
7.0–10.4
CNN-LSTM-ATT
Huang et al.
2024
ECG+PPG+deriv.
CNN + BiLSTM + Attention
10-fold subj.-indep.
~16–18 (ABP wvfm)
~8–10 (ABP wvfm)
UTransBPNet_Demo_In
Huang et al.
2024
ECG+PPG+demographics
U-Net+Transformer+Cross-Attn
10-fold subj.-indep.
10.38 (ABP waveform)
PCC: 0.89
AAMI Clinical Standard: SBP MAE <5 mmHg, SDE <8 mmHg. Best published result: 9.4 mmHg SBP (calibration-based) — still ~2× the clinical threshold. Calibration-free and OOD results reveal severe generalization gaps, confirming cuffless BP estimation remains an unsolved clinical problem. ★ = best result with subject calibration.

## Slide 11
Comparative Analysis — Models & Protocols
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
PPG-Only vs PPG+ACC (HR on DaLiA)
Best PPG-only: BeliefPPG 3.57 bpm
Best PPG+ACC: EnhancePPG 3.54 bpm
→ Gap is surprisingly small (~1%)
→ BeliefPPG achieves parity via temporal HR modeling
→ During high-motion (running, stairs): PPG+ACC is strongly superior
→ PPG-only preferred for ring/earbud wearables
Deep Learning vs Classical DSP
SpaMaPlus (2019 classical): ~9 bpm LOSO
CNN Ensemble (2019 DL): ~7 bpm
EnhancePPG (2025 DL): 3.54 bpm
→ Deep learning: 60%+ improvement over classical
→ DL generalizes better (no parameter re-tuning per subject)
→ DL is deployable with NAS+quantization on MCUs
Impact of Evaluation Protocol — PulseDB (XResNet1d101)
Calibration-Based
SBP: 9.4 mmHg
DBP: 6.0 mmHg
Optimistic — sees subjects during training
Calibration-Free
SBP: 14.0 mmHg
DBP: 8.5 mmHg
Realistic — completely unseen subjects
Out-of-Distribution
SBP: 15–25 mmHg
DBP: 7–10 mmHg
Worst case — different clinical dataset
AAMI Target
SBP: <5 mmHg
DBP: <5 mmHg
Clinical grade standard (not yet achieved)

## Slide 12
Performance Trends: 6 Years of HR Estimation Progress
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
2
4
6
8
10
MAE (bpm)
9
SpaMaPlus
(Classical)
2019
7
CNN Ensemble
(DeepPPG)
2019
6.5
CorNET
2019
4.41
Q-PPG
2021
3.84
Embedding TCN
2022
3.57
BeliefPPG
2023
4.03
PULSE
2025
3.54
EnhancePPG
2025
Classical DSP
PPG+ACC (DL)
PPG-Only (DL)
Best 2025

## Slide 13
Research Challenges in PPG-Based Monitoring
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
~ Motion Artifacts
Wrist movements create noise 10× cardiac amplitude. ACC-based removal assumes linear correlation — violated during complex motions. Frequency overlap (1–3 Hz) between cardiac HR and exercise frequency makes spectral separation unreliable. Deep learning learns implicit suppression but fails on OOD motion patterns.
↔ Cross-Subject Generalization
PPG morphology varies widely across subjects: skin tone, vessel depth, subcutaneous fat, arterial compliance. Per-subject MAE range in PPG-DaLiA spans 2–12 bpm (LOSO). OOD generalization on PulseDB external datasets: SBP MAE degrades from 9 to 15–25 mmHg. Fundamental dataset shift problem.
! Dataset Bias
PPG-DaLiA: young healthy adults (21–55). PulseDB: ICU patients with pathological hemodynamics. Neither represents the real-world wearable target population of elderly hypertensive patients. Models trained on clinical data fail on ambulatory consumer data.
∫ Calibration Requirements
BP estimation without individual calibration remains far from clinical standards. PulseDB: calibration-free MAE 14 mmHg vs. calibration-based 9.4 mmHg (AAMI target: <5 mmHg). Each mmHg of BP error matters clinically — hypertension diagnosis threshold is 130/80 mmHg.

## Slide 14
Robust Physiological Monitoring from Noisy Wearable PPG Signals
Research Vision · Roadmap · Business Impact
SLIDE 1 OF 2
⚡ PROBLEM STATEMENT
Signal Challenges
Motion artifacts
Sensor placement noise
Environmental interference
Limited labelled data
Research Challenges
Robust HR estimation
Cuffless BP estimation
ECG-free wearable approach
On-device hardware constraints
💡 PPG enables continuous monitoring · No ECG required · Scalable wearable deployment
📱 BUSINESS RELEVANCE — Wearable Ecosystem
Depends On
Reliable physio monitoring
Low-power on-device AI
Scalable health analytics
Enables
Continuous cardiovascular monitoring
Remote health tracking
Preventive healthcare
Target Platforms
⌚ Smartwatches
💍 Smart rings
📱 Mobile health apps
🔬 FOUNDATION MODEL VISION
PPG Foundation Model → Physiological Intelligence
Heart Rate
Blood Pressure
Respiration Rate
Arrhythmia
Stress Level
Unified model for all wearable health parameters
Multi-task learning improves individual task robustness
Single deployment artifact reduces device footprint
Vision: One PPG model · All physiological signals · All wearable platforms
🎯 RESEARCH TARGETS & OUTCOMES
Target | Focus Area | Expected Outcome
T1 — SSL Framework | Cross-domain SSL · noisy PPG | Robust HR from real-world wrist signals
T2 — Foundation Model | Multi-parameter physiological model | HR · BP · Respiration · Arrhythmia · Stress
T3 — Lightweight Model | Wavelet-based on-device model | Smartwatch-ready real-time inference
T4 — Patent | Novel wearable monitoring algorithm | IP protection · commercialisation pathway

## Slide 15
Robust Physiological Monitoring from Noisy Wearable PPG Signals
Slide 1 of 2 | Research Vision · Progress · Roadmap
WEARABLE AI
R&D UPDATE
❶ PROBLEM STATEMENT
Photoplethysmography (PPG) is the primary sensing modality in modern smartwatches for physiological monitoring.
Wrist-worn PPG signals are heavily corrupted by motion artifacts, sensor placement variations, and ambient noise.
Reliable extraction of Heart Rate (HR) and Blood Pressure (BP) from noisy wearable PPG remains an open research problem.
Primary Goal: Develop robust algorithms for HR & BP estimation from noisy wrist PPG — requiring noise-robust representations, cross-dataset generalization, and on-device deployability.
❷ BUSINESS RELEVANCE — Smartwatch & Mobile Health
Reliable HR/BP directly powers health monitoring features, remote cardiovascular tracking, and preventive care alerts in consumer wearables.
More accurate algorithms enable improved health analytics reliability and broader deployment across smartwatch and smartphone platforms.
Research underpins next-generation AI-driven health features: continuous BP monitoring, real-time arrhythmia detection, population-level screening.
❸ RESEARCH PROGRESS — 6-Month Plan (2/6 months complete)
2 months
Remaining: 4 months
Cross-domain self-supervised learning (SSL) framework for PPG developed and integrated.
PPG-DaLiA and PulseDB datasets ingested; full preprocessing and windowing pipeline implemented.
Architecture components complete: temporal encoder (CNN+BiLSTM+Attention), contrastive learning,
Evaluation framework built for HR (LOSO) and BP estimation tasks. | Paper preparation in progress.
❹ FUTURE DIRECTION 1
Physiological Foundation Model
Build a general-purpose PPG foundation model using current architecture as base.
Pre-train on larger multi-dataset PPG collections to learn generalized physiological representations.
Applications: HR estimation, BP prediction, cardiovascular risk monitoring.
❺ FUTURE DIRECTION 2
Lightweight On-Device Deployment
Incorporate wavelet-based signal representations and dynamic signal decomposition for efficient feature extraction.
Design lightweight neural models optimized for HR/BP inference on smartwatches and mobile processors.
Target outcomes: reduced compute cost, improved energy efficiency, real-time wearable deployment.
PPG — Photoplethysmography | HR — Heart Rate | BP — Blood Pressure | LOSO — Leave-One-Subject-Out | SSL — Self-Supervised Learning

## Slide 16
Current Work and State-of-the-Art in PPG-Based HR Estimation
Framework Summary · SoTA Comparison · Your Row Ready to Fill
SLIDE 2 OF 2
CURRENT WORK
Self-Supervised Representation
Learning for Noisy PPG
Component | Details
Datasets | PPG-DaLiA · PulseDB
Preprocessing | Bandpass · z-score norm
SSL Framework | Cross-domain self-supervised
Encoder | CNN + BiLSTM + Attention
Contrastive | NT-Xent · instance-level
 | r→ M → NT-
R | 
Tasks | HR estimation · BP estimation
Status | 📝 Paper writing in progress
RECENT STATE-OF-THE-ART — PPG-Based HR Estimation
Model | Authors | Year | Input | Architecture | Feature Extraction | Protocol | MAE (bpm) | RMSE (bpm) | Venue
SpaMaPlus | Reiss et al. | 2019 | PPG + ACC | Sparse spectral / classical DSP | Spectral decomposition | LOSO | ~9.0 | N/R | Sensors (MDPI) 19(14)
DeepPPG CNN | Reiss et al. | 2019 | PPG + ACC | CNN ensemble (multi-head) | STFT of PPG & ACC | LOSO | ~7.0 | N/R | Sensors (MDPI) 19(14)
ResNet50-TL | Dark et al. | 2022 | Wrist PPG 64Hz | ResNet50 (transfer learning) | 2D spectrogram (STFT) | LOSO | 7.28 ± 3.5 | N/R | UbiComp/ISWC '22 ACM
SPEAR | Ghorbani et al. | 2024 | PPG (denoised) | SSL autoencoder + CNN | Self-supervised reconstruction | Subject-split | 5.36 (OOD) | N/R | Harvard HDSR 2024
PULSE | Kasnesis et al. | 2025 | PPG + ACC | Lightweight TCN + cross-attention | Temporal + attention fusion | LOSO | 4.03 | N/R | IEEE JBHI 2025
Proposed (Ours) | — | 2025 | Wrist PPG | Cross-domain SSL: CNN+BiLSTM+Attn | Contrastive + Freq + Masked | LOSO | TBD | TBD | Under Preparation
N/R = Not Reported · LOSO = Leave-One-Subject-Out · OOD = Out-of-Distribution · Proposed row pre-filled — update MAE/RMSE once experiments complete
PPG — Photoplethysmography · HR — Heart Rate · BP — Blood Pressure · SSL — Self-Supervised Learning · JBHI — IEEE Journal of Biomedical & Health Informatics

## Slide 17
Future Research Directions
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
01
Foundation Models for PPG
Pre-train on millions of PPG recordings via masked autoencoding or contrastive learning. Fine-tune for HR, BP, SpO2, RR with minimal labels. SiamQuality (2024), SimPer represent early steps. Target: cross-population, cross-device generalization.
02
Self-Supervised & Weakly Supervised Learning
EnhancePPG (2025) showed 12% MAE reduction from self-supervised pre-training. SPEAR (2024) achieved OOD generalization without labeled DaLiA data. Large unlabeled wearable databases (>100M hours) offer untapped potential for pretraining.
03
Multi-Site Sensor Fusion
Combine ring (finger), earlobe, wrist, forehead PPG signals. Different PTT paths → richer BP information. Graph neural networks or attention fusion for dynamic quality-weighted aggregation. τ-Ring dataset (2025) demonstrates ring-form potential.
04
Edge AI & TinyML
Q-PPG: 1.9 kB, 1.79 mJ. PULSE student: 37.9 kB, 0.577 mJ. Target: <10 kB, <0.1 mJ for CR2032 battery operation. Hardware-aware NAS + INT4 quantization + structured pruning. Neural ODE / implicit networks for extreme compression.
05
Physiological Hybrid Models
Windkessel hemodynamic constraints + neural networks (PMB-NN). BeliefPPG temporal HR priors as model. Arterial stiffness indices from PPG morphology (APG, stiffness index SI). Interpretable BP estimation with physiological guarantees.
06
Clinical Validation & Standardization
Achieve AAMI/ISO 81060-2 standards for BP (<5 mmHg MAE, <8 mmHg SD). Large prospective clinical trials with diverse populations (age, sex, ethnicity, comorbidities). Standardized protocol: LOSO or larger multi-site cross-dataset evaluation.

## Slide 18
Verified References — IEEE Format
PPG-DaLiA & PulseDB | Biomedical AI Research Report | March 2026
[1] A. Reiss et al., 'Deep PPG: Large-Scale HR Estimation with CNNs,' Sensors, 19(14):3079, 2019. DOI: 10.3390/s19143079
[2] D. Biswas et al., 'CorNET: Deep Learning for PPG-Based HR,' IEEE TBCAS, 13(2):282-291, 2019. DOI: 10.1109/TBCAS.2019.2892297
[3] A. Burrello et al., 'Q-PPG: Energy-Efficient HR on Wearables,' IEEE TBCAS, 15(6):1196-1209, 2021. DOI: 10.1109/TBCAS.2021.3122017
[4] A. Burrello et al., 'Embedding TCNs for PPG-based HR,' ACM HEALTH, 3(2), 2022. DOI: 10.1145/3487910
[5] J. Bieri et al., 'BeliefPPG: Uncertainty-aware HR from PPG,' UAI 2023, PMLR 216:173-183. arXiv:2306.07730
[6] P. Kasnesis et al., 'PULSE: Attention for PPG HR,' IEEE JBHI, 2025. DOI: 10.1109/JBHI.2025.3580474
[7] L. Benfenati et al., 'EnhancePPG: Self-Supervised PPG HR,' AICAS 2025. arXiv:2412.17860
[8] C. Kechris et al., 'KID-PPG: Knowledge-Informed HR,' arXiv:2405.09559, 2024
[9] E. Dark et al., 'HR from Noisy PPGs: Transfer Learning,' UbiComp/ISWC 2022. DOI: 10.1145/3544793.3563407
[10] R. Ghorbani et al., 'SPEAR: Self-Supervised PPG Denoising,' HDSR, Issue 6.3, 2024
[11] W. Wang et al., 'PulseDB: Large BP Benchmarking Dataset,' Front. Digital Health, 4:1090854, 2023. DOI: 10.3389/fdgth.2022.1090854
[12] M. Moulaeifard et al., 'Generalizable DL for PPG-Based BP,' arXiv:2502.19167, 2025
[13] S. Huang et al., 'Validation of DL for Cuffless BP on PulseDB,' Cardiovasc. Health Tech., 2024
[14] J. Gao et al., 'UTransBPNet for Cuffless BP,' Sci. Rep., 2025. DOI: 10.1038/s41598-025-02963-3
[15] M. Risso et al., 'Robust & Energy-efficient PPG HR,' IEEE ISCAS 2021. DOI: 10.1109/ISCAS51556.2021.9401282
[16] L.G. Rocha et al., 'Binary CorNET: MCU PPG HR,' IEEE TBCAS, 14(4):715-726, 2020. DOI: 10.1109/TBCAS.2020.3001675

## Slide 19
Key Takeaways
1
HR on PPG-DaLiA: 60%+ improvement since 2019 (SpaMaPlus 9.0 → EnhancePPG 3.54 bpm LOSO)
2
PPG-only can match PPG+ACC (BeliefPPG 3.57 vs EnhancePPG 3.54) via temporal probabilistic modeling
3
BP on PulseDB: Best calibration-based result 9.4 mmHg SBP — still ~2× clinical AAMI standard (<5 mmHg)
4
Evaluation protocol matters: random-split inflates performance; LOSO and calibration-free give honest estimates
5
Self-supervised pre-training + NAS + knowledge distillation are the key drivers of recent progress
6
Edge deployment is achievable: Q-PPG 1.9 kB / 1.79 mJ; PULSE student 37.9 kB / 0.577 mJ on MCUs
7
Open challenges: domain shift, cross-population generalization, and truly calibration-free BP estimation
Biomedical AI Research Report | March 2026 | All citations verified