## Slide 1
Agentic PPG Analysis System
Industry-Level Observe → Plan → Act → Reflect Loop
Model: Ollama 2B (phi / gemma:2b / qwen2:1.5b) Dataset: WESAD (wrist PPG)
BVP @ 64 Hz · ACC @ 32 Hz · 15 Subjects · 10-second windows

## Slide 2
Agenda
01
Problem & Motivation
02
What Makes It Truly Agentic?
03
System Architecture
04
The Observe→Plan→Act→Reflect Loop
05
Tool Registry & Signal Processing Fixes
06
Prompt Engineering for 2B Models
07
Before vs After: Code Improvements
08
Results & Output Demo
09
Limitations & Next Steps

## Slide 3
Problem & Motivation
The Challenge
➤ PPG signals contain noise, motion artefacts & DC drift
➤ 15 subjects × 100 windows = massive data throughput
➤ Clinicians need adaptive, explainable summaries
➤ Small LLMs (2B) hallucinate on vague prompts
➤ Single-turn scripts can't react to analysis failures
Agentic Solution
✔ Normalised bandpass + prominence filtering
✔ Orchestrator spawns one agent per subject
✔ LLM generates structured clinical reports
✔ Constraint-heavy prompts + JSON fallback
✔ Reflect step detects & retries bad reports

## Slide 4
What Makes It Truly Agentic?
🛠️ Tool Registry
5 registered tools — load, classify, report, reflect, qa — each callable by name
🧠 LLM Planning
Agent uses LLM to select the next tool from an allowed set, not hard-coded branching
🔄 Reflect Loop
After report generation, agent evaluates output vs data and auto-retries on mismatch
💾 State Memory
AgentState persists HR, motion, classification, and rolling QA history across steps
👤 HITL Checkpoints
Human approves style and chats with agent; agent grounds all answers in data

## Slide 5
System Architecture
🏭 ORCHESTRATOR — iterates S1 … S15, spawns fresh PPGAgent per subject
PPGAgent
1
OBSERVE
tool_load_signal()
BVP bandpass → peak detect → HR
ACC RMS motion
2
PLAN
LLM picks next tool
from [classify, report]
given observation
3
CLASSIFY
tool_classify()
LLM → JSON {condition,
activity, reliability}
4
REPORT
HITL: style choice
tool_report()
short / long clinical
5
REFLECT
tool_reflect()
LLM checks data match
auto-retry on fail
📦 AgentState — HR, STD, Motion, Classification, Report, QA History
👤 HITL — style picker (step 4) + open QA loop (step 5)

## Slide 6
The Observe → Plan → Act → Reflect Loop
OBSERVE
Load PKL
Extract features
PLAN
LLM selects
next tool
ACT
Classify +
Generate report
REFLECT
LLM validates
report vs data
HITL
Human approves
or asks doubts
Agent
Loop

## Slide 7
Tool Registry & Signal Processing Fixes
Tool | Type | What It Does
tool_load_signal | Deterministic | Bandpass → normalise → peak detect → RMS motion → physio gate
tool_classify | LLM + fallback | HR condition + activity → JSON with regex fallback
tool_report | LLM | Short/long clinical summary (2B-safe prompt)
tool_reflect | LLM | Validates report vs data; triggers retry on mismatch
tool_qa | LLM + memory | Grounded Q&A with 3-turn rolling history
Key Signal Fixes
✗ find_peaks(ppg, distance=FS*0.4) — no normalise
✔ Z-score normalise first; prominence=0.3, height=0.1
✗ No RR interval validation
✔ Filter RR ∈ [0.3 s, 1.5 s] → removes motion artefacts
✗ acc[int(start*32/64)] (magic number)
✔ acc[s//ratio:(s+win)//ratio] + explicit ACC_FS=32
✗ np.sqrt(np.sum(acc**2, axis=1))
✔ np.linalg.norm(acc, axis=1) → then RMS

## Slide 8
Prompt Engineering for 2B Models
🔢 Feed rule-based hints
Pre-compute hr_label / motion_label in Python; give to LLM as context — reduces reasoning load
📦 Force JSON schema
Paste the exact JSON template in the prompt; LLM fills blanks instead of free-generating
🔍 Regex fallback
_safe_json() extracts first {…} from output using re.search — survives any preamble text
🌡️ Temperature = 0.1
Near-deterministic output — avoids random style switches between runs
✂️ Context ≤ 120 tokens
2B context window is tiny; keep prompts under 120 tokens for reliable instruction-following
🔄 Reflect as guardrail
tool_reflect() asks a binary ok/issue question — even 2B handles binary classification well

## Slide 9
Before vs After — Code Improvements
Aspect | Original Code | Improved Code
Architecture | Procedural script, no tool concept | Tool Registry + AgentState + PPGAgent class
Peak detection | Raw BVP, distance only | Z-score normalise + prominence + RR gate
ACC indexing | int(start * 32 / 64) — magic number | s // ratio with explicit ACC_FS=32 constant
Prompts | Long multi-line templates, no constraints | ≤ 120-token prompts + JSON schema + fallback
LLM planning | Absent — hard-coded if/elif flow | _plan() — LLM selects tool from allowed set
Error recovery | None | Reflect step auto-retries report generation
Memory | None | Rolling 3-turn QA history in AgentState
Output | Raw LLM text | Structured card (HR ± STD, condition, activity)

## Slide 10
Output Demo — Subject S1
════════════════════════════════════════════
🤖 AGENT › S1 [phi]
════════════════════════════════════════════
📡 [1/5] Observe — loading signal…
└─ HR=74.3±8.1bpm Motion=1.82 ValidWin=87/100
🧠 [2/5] Plan — agent selecting next action…
└─ Selected: classify
⚙️ [3/5] Act — classify HR & activity…
└─ Condition:normal Activity:light Reliability:high
📋 Report style (short/long) [short]: short
📝 [4/5] Act — generating report…
🔍 [5/5] Reflect — evaluating report quality…
└─ ✅ Report consistent with data
❓ Any doubts? (yes/no) [no]: no
✅ Agent done — S1

## Slide 11
Limitations & Next Steps
⚠️ Current Limitations
➤ 2B models have < 2B param reasoning — JSON fallback is essential
➤ WESAD only covers 15 subjects — limited generalisability
➤ Single reflect retry — persistent hallucinations not fully handled
➤ No cross-subject memory — agent forgets prior subjects
🚀 Next Steps
➤ Swap to Claude / GPT-4o API for richer planning & function-calling
➤ Add vector-store (Chroma) to persist & query subject histories
➤ HRV features (SDNN, RMSSD, pNN50) for deeper analysis
➤ Anomaly detection tool — agent invokes on high STD or motion
➤ Streaming output for real-time clinical dashboard

## Slide 12
Key Takeaways
1. Agentic = Tool Registry + LLM Planning + Reflect loop, not just an LLM + prompt
2. 2B models need short prompts, JSON schemas, and deterministic fallbacks
3. Signal quality matters: normalise + prominence filter + RR gating = reliable HR
4. HITL checkpoints keep the agent safe for clinical / research use
5. This architecture scales: swap Ollama for any API model with zero structural change
Questions?